## Slide 1: Section VI
Earthing and Grounding

## Slide 2
Core Topics
(i) Earthing
(ii) Grounding
(iii) Convention for the Flow of Current

## Slide 3
Earthing:
Earthing is a safety feature for electrical appliances. Metal parts, not used in the internal circuitry (e.g. chassis) are connected to the earth via an earth wire (green and yellow).
If, due to a circuit fault (corrosion, faulty manufacture, mice gnawing at cables, etc.), one of the ‘live’ wires comes into contact with the metal there is a significant risk to the user who may get an electric shock.

## Slide 4
Earthing:
If the metal (chassis) is earthed, this danger is averted since the current will flow to the earth via the earth wire as this is the path of least resistance (as opposed to flowing through the human body).
There are two other wires in the mains cables – ‘live’ (brown) and ‘neutral’ (blue).
The earth itself is at zero electrical potential and acts as a current sink. Other examples of earthing are lightning rods and static dischargers in cars.

## Slide 5
Earthing:
The electrical symbol for earth is:

## Slide 6
Grounding:
Grounding has a very different meaning to earthing and it is essential to understand the concept of grounding because it is of great practical importance. Consider the following setup with a 5V supply:
In this isolated setup there is a potential difference of 5V across the supply and R.
5Volts
0Volts

## Slide 7
Grounding:
However the absolute potentials (with respect to earth – 0V), may be:
15Volts
10Volts

## Slide 8
Grounding:
505Volts
500Volts

## Slide 9
Grounding:
In all cases the same current flows – i.e. it is the potential difference across the supply (and consequently the load) that is important when determining the current flow in a network. The absolute potentials are irrelevant for this purpose.
For simplicity of analysis, we assign the ‘return’ or bottom wire a potential of zero volts. We call this the ground wire or ‘zero reference’.

## Slide 10
Grounding:
A good analogy is that with cartography, where terrain height is measured with respect to sea level. It is important to remember that ground does not necessarily have the earth’s zero electrical potential.
In short, Ground = Zero Reference.
The electrical symbol for ground is:

## Slide 11
Convention for the Flow of Current:
By convention current is said to flow from regions of positive electrical potential to regions of relatively negative potential.
In fact current is normally the case of negatively charged electrons flowing from negative to positive. However, the convention stands.