## Slide 1: Section III
Sources and Instrumentation

## Slide 2
Student Online Teaching Advice Notice
The materials and content presented within this session are intended solely for use in a context of teaching and learning at Trinity.
Any session recorded for subsequent review is made available solely for the purpose of enhancing student learning.
Students should not edit or modify the recording in any way, nor disseminate it for use outside of a context of teaching and learning at Trinity.
Please be mindful of your physical environment and conscious of what may be captured by the device camera and microphone during videoconferencing calls.
Recorded materials will be handled in compliance with Trinity’s statutory duties under the Universities Act, 1997 and in accordance with the University’s policies and procedures.
Further information on data protection and best practice when using videoconferencing software is available at https://www.tcd.ie/info_compliance/data-protection/.
© Trinity College Dublin 2020

## Slide 3
Core Topics
(i) Voltage and Current Sources
(ii) Ideal and Non-Ideal Sources
(iii) Internal resistance
(iv) Instrumentation

## Slide 4
Voltage and Current Sources:
Two types of electrical power sources are available:
1) Voltage Sources 2) Current Sources
Ideal Sources:
An ideal voltage/current source will provide a stable voltage (dc or ac)/stable current (dc or ac) regardless of the circuit it is supplying.

## Slide 5
Voltage and Current Sources:
Ideal Voltage Sources:
The ideal voltage source is a two-terminal element with the property that the voltage across its terminals is specified at every instant in time and does not depend on the current flowing through it.
Ideal Current Sources:
An ideal current source is a two-terminal element with property that the current flowing through it is specified at any instant in time and does not depend on the load connected to it.

## Slide 6
Voltage and Current Sources:
Electrical Symbols:
Ideal DC Voltage Source:
Cell/Battery (non-ideal source):

## Slide 7
Voltage and Current Sources :
AC Voltage Source (ideal):
Current Source (ideal)

## Slide 8
Voltage and Current Sources :
Deviation from the Ideal:
In practice, sources are not ideal. Sometimes sources can be well modelled or assumed to be ideal – the mains for example. Other times it cannot – a battery near depletion or having a high current drawn from it is not an ideal scenario. The deviation from the ideal is well modelled using a resistor (known as the ‘internal resistance’ of the non-ideal source) in series with the ideal source (for voltage sources). (For current sources the resistor is placed in parallel)

## Slide 9
Internal Resistance:
A battery (non-ideal source) modelled as an ideal source and a series resistor (known as the internal resistance of the source):
If RInternal is small enough to be ignored, then we can simply consider the source to be ideal.
Note: An ideal voltage source has zero internal resistance.

## Slide 10
Instrumentation:
The Ammeter measures current. It is connected in series:
The Voltmeter measures potential difference. It is connected in parallel:
The Ohmmeter measures resistance. It is connected in parallel:
Read up on these topics in Meade and Boylestad.
A
V